## Slide 1: FIRE SAFETY
Operating Room Suite

## Slide 2: A SURGICAL FIRE…
Is a fire in, on, or around a patient who is undergoing a medical or surgical procedure
Is considered a sentinel event & preventable
65% of surgical fires occur on the head, neck, face and upper trunk

## Slide 3: SURGICAL FIRE TRIANGLE
3 Main Contributing Factors

## Slide 4: Room air can be used in surgeries such as:
Tracheostomies
Tonsillectomies
Bronchoscopies

## Slide 5: Flash Fire
30% O2 needed to start a flash fire
Clinicians can reduce the risk of surgical fires by maintaining oxygen levels below 30%
Minor elevations in oxygen concentration as a result of supplemental oxygen and/or surgical drapes result in an astronomically increased risk for fire.
Notes: Operating Room Fires | Anesthesiology | American Society of Anesthesiologists (asahq.org)

## Slide 6: Flash Fire
Reduce risk by:
  Blending oxygen with room air to decrease the concentration of oxygen delivered to the patient
  Diluting the under drape area space with air via the anesthesia circuit
  Using modified draping techniques that allows for increased air flow in the under drape area.
Notes: Operating Room Fires | Anesthesiology | American Society of Anesthesiologists (asahq.org)

## Slide 7: WAITING GAME
Wait to drape or start surgery at least
3 minutes or until the alcohol-based prep is dry to help minimize the risk for surgical fire

## Slide 8: IF A SURGICAL FIRE STARTS…
Immediately shut off all oxygen/nitrogen supply to the patient
Immediately remove burning drapes from the patient and douse the fire and the patient with saline to put the fire out.
Use a fire extinguisher on the drapes if necessary

## Slide 9: PREVENTING FIRES IN THE OROPHARYNX…
decrease oxygen concentration below 30%
suction oropharynx before using electrocautery device
use metal suction device instead of plastic one.

## Slide 10: P.A.S.S
PASS is a mnemonic used to remember the four basic steps for using a fire extinguisher
    Pull the pin
    Aim at the base of the fire
    Squeeze the handle of the extinguisher
    Sweep back and forth until the fire is extinguished

## Slide 11: R.A.C.E
In case of a fire, you should follow the R.A.C.E. fire procedure
    Rescue/Remove: Rescue or remove any persons from the immediate scene.
    Alert/Activate: Pull the nearest alarm and call 2000.
    Confine: Close all doors to the hazard or fire area.
    Extinguish/Evacuate: Extinguish the fire using a fire extinguisher or evacuate the area

## Slide 12: O.R. FIRE EXTINGUISHER LOCATIONS
MAIN OR:
Next to the elevator that goes up to the overflow supply room
Outside room 9 next to the exit stairwell
Outside room 7 next to the main pyxis room
Next to the stairwell by the c.v. room
Main OR doors left side on the wall
WSOP OR:
Outside Room 2 by pyxsis

## Slide 13: MEDICAL GAS SHUT OFF VALVE LOCATIONS
Outside each OR room on the wall

## Slide 14
WSOP EMERGENCY EXIT

## Slide 15
MAIN OR EMERGENCY EXIT

## Slide 16
SEE SOMETHING SAY SOMETHING
Each member of the surgical team is responsible for assessing all hazards that could contribute to a surgical fire, as well as observing the action of all other team members and speaking up immediately if any preventive risk or evidence of a possible fire is observed.

## Slide 17: Continue to the Test
Link
https://forms.office.com/r/Vvx91DXLj9